## Slide 1: Wheel Assembly Layout Proposal
Project Velocity: Aurora Express
Created By Muhammad Hassan Bin Sohail

## Slide 2
TASK 1
Time Study Analysis Of Aurora Express Wheel Assembly

## Slide 3
Task 1: Time Study Methodology
What Is a Time Study?
A time study measures the time taken by a skilled operator to perform each step of a defined process at a standard pace. The goal is to identify inefficiencies, establish standard times, and pinpoint bottlenecks for improvement.
In this task, a time study of the Aurora Express Wheel Assembly process is conducted. Across the wheel assembly section there are 10 observations recorded for each of the 20 assembly steps.
Key Analytical Tools Used
Average (mean) duration per step
Standard Deviation to spread of observations
Range to compare best vs worst case per step
Coefficient of Variation (CV%) to check relative inconsistency
Weighted Composite Score to combine duration (70%) with CV (30%)
At a Glance
20
Assembly Steps Studied
10
Observations per Step
3,724 s
Total Seconds per Cycle
01:02:04
Total Cycle Time

## Slide 4
Task 1 — Statistical Analysis of All 20 Steps
⭐ Primary Bottleneck ★ Removed in Task 2 proposed layout Orange = High CV (>10%)
Step No. | Element Description | Avg (sec) | Avg (mm:ss) | Std Dev | Range(s) | CV (%) | Rank
1 | Retrieve wheel components from storage | 147.5 | 02:28 | 5.80 | 20.00 | 3.93 | 20.00
2 | Setup workspace and tools | 98.9 | 01:39 | 6.42 | 17.00 | 6.49 | 19.00
3 | Inspect components for defects | 182.7 | 03:03 | 6.52 | 18.00 | 3.57 | 18.00
4 | Assemble hub to wheel frame | 256.8 | 04:17 | 8.12 | 28.00 | 3.16 | 4.00
5 | Secure hub with bolts | 168 | 02:48 | 9.07 | 25.00 | 5.40 | 12.00
6 | Lubricate wheel bearings | 90.1 | 01:30 | 10.81 | 29.00 | 11.99 | 1.00
7 | Install bearings into hub | 188.3 | 03:08 | 7.42 | 19.00 | 3.94 | 14.00
8 | Attach wheel sensors | 158 | 02:38 | 7.35 | 21.00 | 4.65 | 17.00
9 | Test sensor functionality | 176.9 | 02:57 | 8.46 | 26.00 | 4.79 | 13.00
10 | Fit brake discs to hub | 241.2 | 04:01 | 8.13 | 23.00 | 3.37 | 6.00
11 | Install brake calipers | 227.5 | 03:48 | 8.45 | 27.00 | 3.71 | 9.00
12 | Connect brake lines | 213.3 | 03:33 | 8.15 | 26.00 | 3.82 | 10.00
13 | Bleed brake system | 238.3 | 03:58 | 8.59 | 25.00 | 3.60 | 5.00
14 | Mount wheel to axle | 324.5 | 05:25 | 7.79 | 23.00 | 2.40 | 1.00
15 | Secure wheel with locking mechanism | 136.5 | 02:16 | 9.20 | 30.00 | 6.74 | 11.00
16 | Conduct wheel alignment | 284.8 | 04:45 | 9.66 | 26.00 | 3.39 | 3.00
17 | Perform functional test of wheel assembly | 191.8 | 03:12 | 10.25 | 28.00 | 5.34 | 8.00
18 | Clean assembly area | 116.3 | 01:56 | 7.53 | 25.00 | 6.47 | 16.00
19 | Document assembly process | 123.7 | 02:04 | 7.94 | 23.00 | 6.42 | 15.00
20 | Transport assembly to next section | 159.2 | 02:39 | 10.64 | 30.00 | 6.69 | 7.00
⭐
⭐
★

## Slide 5
Task 1 — Bottleneck Findings & Root Cause
Current cycle time
01:02:04
3724.3 seconds per 20 steps
Bottleneck steps
5
2 primary & 3 secondary
Share of Cycle (Bottlenecks)
33.40%
Steps 14, 6, 16, 4, 13
Projected saving
99.79
Conservative estimate
Top 5 Steps by Duration + Actions
#1
Step 14 - Mount wheel to axle
324.5s | Dedicated crane zone (HIGH)
#2
Step 6 - Lubricate wheel bearings
161s | standardize lubrication via calibrated dispensing tool (HIGH)
#3
Step 16 - Align wheel assembly
264s | Implement laser-guided alignment system (MEDIUM)
#4
Step 4 - Assemble hub to wheel frame
256s | SOP standardization (MEDIUM)
#5
Step 13 - Bleed brake system
238.3s | SOP standardization (MEDIUM)
Descriptive Root cause Summary
Why is mounting the slowest step?
Shared crane creates a queue every single cycle
Why is lubrication so inconsistent?
No calibrated tool; operator hand-applies with no fixed quantity
Why does alignment take so long?
Manual visual judgment with no precision tooling
Why do hub assembly and brake bleeding vary by operator?
No SOPs exist for either step; experience and informal training drive performance

## Slide 6
Task 1: Composite Priority Score (Duration 70% + CV 30%)
Chart: 
| S1 | S2★ | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11 | S12 | S13 | S14⭐ | S15 | S16 | S17 | S18 | S19 | S20
Composite Score | 0.2 | 0.23 | 0.4 | 0.4 | 0.32 | 0.5 | 0.29 | 0.26 | 0.31 | 0.37 | 0.36 | 0.34 | 0.38 | 0.7 | 0.11 | 0.613 | 0.37 | 0.16 | 0.23 | 0.37
How to Read This
Score = (0.7 × Normalised Duration) + (0.3 × Normalised CV)
Higher score = higher priority for improvement action.
Step 14 (0.70) is the clear primary bottleneck — structural delay confirmed by low CV.
Step 16 (0.61) is the second priority — duration + alignment variability.
Step 6 (0.50) scores mid-range despite being the shortest step — its 12% CV makes it a consistency risk.
★ Step 2 is excluded in the proposed layout (assembly line setup removes per-cycle workspace setup).

## Slide 7
TASK 2
Reconfiguring Assembly Line Layout changes while implementing actions for recognized bottlenecks

## Slide 8
Work Area
Crane

## Slide 9: Original Layout
WHEEL
PRESS
ASSEMBLY 1
WAREHOUSE
ASSEMBLY 3
ASSEMBLY 4
Crane
ASSEMBLY 2
61:15
62:35
62:25
61:47
62:10
62:43
61:46
62:52

## Slide 10
Task 2: Current Layout: How It Contributes to the Bottleneck
Original Layout (Clustered)
Problems with this layout:
Crane shared across all 4 stations → Step 14 always waits
Non-linear flow → workers cross the floor between steps
Warehouse distant from assembly start → Step 1 travel time
Step 2 (setup) needed every cycle — pure non-value-added time
Proposed Layout (Linear + Dedicated Crane)
Improvements:
Dedicated crane zone for Step 14 → no more queue time
Linear product flow → zero cross-floor movement
Step 2 eliminated → workstations permanently configured
Warehouse at process start → immediate component access
Setup & Inspection area is next to the warehouse → for Step 3
Finished product holding are is introduced → for Step 20

## Slide 11: Proposed Layout
Station 4:
Wheel press
Station 3: Brake System
WAREHOUSE
Station 5: Wheel Alignment
Station 6: Testing
Dedicated Crane
Station 2: Hub & Wheel Assembly
02:27
Crane
Setup & Inspection station
Station 7: Finished product Holding Area
Task 1
Task 3
03:02
Task 4 – Task 9
17:05
Task 10 – Task 13
15:08
Task 14
04:36
Task 15 – Task 16
Task 17 – Task 18
06:39
05:08
02:39
Task 20

## Slide 12
Task 2 — Impact Summary & Implementation Plan
~99.79s
Step 14 — Dedicated Crane (PRIMARY)
~99s
Step 2 Eliminated (Assembly Line)
~198.79s
Total Saving Per Unit (~5.33%)
Before: 01:02:04 (3,724 sec)
Original 20-step clustered layout with shared crane and per-cycle workspace setup.
After: ~56:44 (3,404 sec)
19-step linear layout: Step 2 removed, dedicated crane zone, linear product flow.
Phased Implementation Plan
Phase 1 (Weeks 1–2)
Space modelling & simulation; validate proposed layout digitally before any physical changes
Phase 2 (Weeks 3–4)
Operator training on SOPs; install calibrated lubrication dispensing tool (Step 6 CV fix)
Phase 3 (Weeks 5–6)
Physical reorganisation over planned weekend shutdown; establish dedicated crane zone
Phase 4 (Weeks 7–8)
Follow-up time study; measure all 19 steps vs baseline; confirm ~167s saving per unit

## Slide 13
References
Books & Textbooks
1. Hopp, W. J., & Spearman, M. L. (2011). Factory Physics (3rd ed.). Waveland Press. — When a shared crane is converted to a dedicated resource, queuing delay is eliminated. Reducing resource utilisation from ~90% to ~70% by dedicating a resource cuts average queue time by 50–75%. Applied to Step 14.
Journal Articles & Conference Papers
2. Antil, P., & Budhiraja, N. (2013). Process variability reduction through tooling and fixture modification. International Journal of Engineering Research and Applications, 3(4), 1–6. — Modifying tools and fixtures reduced rejection rate and improved production consistency — mechanism being elimination of operator-dependent variation. A 30–40% CV reduction for a manual dispensing step is consistent with this class of improvement. Applied to Step 6.
3. Diaz, R., et al. (2017). Cycle time study for aircraft wing spar assembly with guided alignment tools. Journal of Manufacturing Systems. — Introducing guided alignment tools replacing manual judgment reduced alignment cycle time by up to 20%. A conservative 10–15% is applied to Step 16 given wheel assembly is a simpler geometry than wing spar.
4. Kumar, S., & Kumar, S. (2014). Reduction of cycle time in truck body assembly using lean principles. International Journal of Industrial Engineering, 21(3), 112–124. — Implementing standardised work instructions reduced cycle time at individual assembly stations — primary mechanism being elimination of operator hesitation and rework. A 5–8% reduction per step is consistent with SOP-only interventions. Applied to Steps 4 and 13.
5. Lathashankar, et al. (2018). Cycle time reduction in a 4-ton compactor assembly using dedicated fixtures. International Journal of Innovative Research in Science, Engineering and Technology. — Introducing a dedicated fixture reduced front chassis cycle time by 20% and rear chassis by 18% — mechanism identical to replacing shared, unscheduled lifting equipment with a dedicated setup. Applied to Step 14.
6. Malik, A., et al. (2011). Industrial engineering cycle reduction techniques focused on equipment allocation. Journal of Engineering and Applied Sciences, 6(8), 1–7. — After implementing equipment allocation improvements, production time was reduced by 24%. A 15–20% estimate for a single step is therefore conservative relative to this precedent. Applied to Step 14.
7. Mishra, R. (2015). Productivity improvement through method study in automobile assembly. International Journal of Engineering and Management Research, 5(2), 308–312. — Standardisation and documented SOPs achieved meaningful cycle time reduction — confirming procedural interventions alone yield 5–10% gains without capital tooling changes. Applied to Steps 4 and 13.
8. Naveen, K., & Ramesh Babu, T. (2015). Cause-and-effect analysis and corrective tooling in manual assembly. International Journal of Advanced Manufacturing Technology, 78(1–4), 341–352. — Production rate improvement of 10–18% documented using corrective tooling on manual assembly steps. Laser alignment is a stronger intervention, so 10–15% is conservative. Applied to Step 16.
9. Shayea, A., et al. (2011). Productivity improvement model without increasing operation risk and fatigue. Journal of Applied Sciences, 11(16), 2909–2916. — Formalising procedure on safety-sensitive steps reduces both time and error rate simultaneously — key mechanism being reduced cognitive load on operators. Applied to Step 13 (brake bleed).
Standards & Technical Documents
10. ISO (2022). ISO 8655: Piston-operated volumetric apparatus — requirements and test methods. International Organisation for Standardisation. — Calibrated dispensing tools reduce inter-operator CV from 10–15% down to 2–5%. A 30–40% reduction in CV is a conservative estimate. Applied to Step 6 (lubrication standardisation).
11. SKF Group & Schaeffler Group (Various). Bearing maintenance and lubrication engineering guides. SKF / Schaeffler technical documentation. — Inconsistent grease quantity is the leading cause of premature bearing failure in wheel assemblies. Standardising to a calibrated dispenser is classified as a low-cost, high-impact intervention. Applied to Step 6.
12. Thermo Fisher Scientific (Various). Pipetting and dispensing application notes — calibrated tool performance data. Thermo Fisher Scientific technical documentation. — Switching from manual to calibrated automated dispensing tools reduces inter-operator CV from 10–15% down to 2–5%. Applied to Step 6 as supporting evidence for lubrication CV reduction target.
13. Toyota Motor Corporation (Various). Toyota Production System — standardised work for fluid-fill and bleed operations. Toyota OEM documentation (publicly referenced in TPS literature). — Standardised work sequences for bleed operations reduce cycle time variance by 30–50% and mean time by 5–10% by eliminating redundant passes and hesitation time. Applied to Step 13.
Note: Percentage estimates are directional benchmarks derived from the principles and findings in the above references, not verbatim figures extracted from a single page. Before formal submission, verify edition details and page numbers via Google Scholar, Wiley Online Library, or your university library database.